VIII - Reconstruction of the Ishtar of Agade Temple

1. Historical building name: A complete reconstruction of the Ishtar of Agade temple 2. Location according to the schematic plan: in the area of Babylonian private houses, at the street that leads at right angle to the Processional Way; the area was called Merkes by R. Koldewey.

3. Lay-out of the historical building: after Mohammed Nasir, The temple of Ishtar of Agad, Sumer XXXV, 1979, No. 1-2, p. 76

4. Description of the present state of preservation: Reconstruction on original walls remnants and foundations; it has rectangular shape, measuring 37,2 x 31 m; main entrance from the South and another one from the East. Around the building the ground is covered with ceramic tiles. A/ Façades: covered with mud plaster with a lot of straw temper. The Northern Façade: Fig. 1 The plaster is cracked; considerable losses on the side walls of the buttresses and close to the ceiling. In the lower part – a strip of 0,5 m high – the plaster is wet, partially has fallen off; below it a cement mortar visible. Close to the roof – the plaster is wet in two places, in other places the plaster is missing, erosion of the bricks occurred. The Eastern Façade: Fig. 2 The plaster cracked and with air bubbles. A strip up to 0,5 m high above the ground level is moist, the plaster has been partially washed away. Some losses of the plaster, especially close to the roof. A crack of the wall (?) to the North of the entrance to the building as well as on the nearby buttress. Near the entrance a modern inscription is scraped on the plaster. There are two drainage pipes for rain water in the upper part of the wall. The Southern Façade: Fig. 3 At the base of the wall – a strip of the plaster 10 – 30 cm wide is missing; the rest of the plaster is wet. There are some air bubbles; detachment of the plaster also occurred. Small losses of the plaster and cracks in the upper part. In a distance of 2 m from the south-eastern corner there is a large crack throughout the whole wall; it is 2 cm wide at the base and 30 cm wide close to the ceiling. In the upper part the whole wall is cracked while at the base the crack has 40 cm in depth. The Western Façade: Fig. 4 At the base of the wall, up to 1 m high above the ground level, the plaster is moist; the upper part of the wall and especially close to the roof the plaster is almost completely washed away, the bricks are clearly visible. Cracks in the plaster, mostly in the lower part. Medium-sized losses in three places; in the northernmost situated loss cement mortar is visible. The lower part of the southernmost buttress are soiled with bird excrement. In some places mortar in joints is missing. There are two drainage pipes for rain water in the upper part of the wall. B/ Roof: Fig. 5 Fig. 6 Covered with baked mud tiles; losses of mortar. Not levelled; numerous hollows and buldges. The top of the four façades are covered from the top and three sides with a wet cement plaster and plaster with admixture of gypsum or lime? The plaster is cracked; some parts are peeling off and in several places they are missing. Fig. 7 Along the eastern edge of the roof there is a serious crack starting in the south-eastern corner and going to the North for a distance of 12 m. Four pipes for draining off rain water are clean. C/ Interior: Locus 1 – Floor: Fig. 8 Small damages of the mortar between the cement (?) tiles. Broken wooden chairs and some sand on the surface. Locus 1 – Ceiling: Fig. 9 The reed mats supported by wooden beams; the whole content moisture. One beams is cracked lengthwise. The reed mats are torn up in several places. Locus 1 – The Northern Wall: Fig. 10 A white gypsum lining, 1,5 cm thick, close to the ceiling is missing. There is some dirt on the gypsum lining; cracks in the lower part, air bubbles and detachment from the wall. The locus 16 doorway: mud plaster with admixture of a cement (?); from both side plaster is unsmoothed, is coming off, especially on the eastern wall. Locus 1 – The Eastern Wall: Fig. 11 Close to the ceiling the gypsum lining, 1,5 cm thick, is missing. The plaster is dirty; some damp patches. In the southern part – a plaster crack almost throughout the wall height, going from the top down. In a strip of 1,2 high above the floor level the plaster is peeling off, there are some air bubbles, and the plaster is falling off. The locus 2 doorway: up to 1,6 m high above the floor level there are some bulges, the plaster is cracked and falling off. Locus 1 – The Southern Wall: Fig. 12 Close to the ceiling the gypsum lining, 1,5 cm thick, is missing. The plaster is dirty; small spider’s webs, damp patches. In a strip up to 1 m high above the floor level – the plaster has a lot of air bubbles, is peeling off and splitting off. The outside doorway: considerable losses of the gypsum lining on both sides as well as singular bricks probably in the places where the front door was fastened. In the lower part the mud plaster is deteriorated and splitting off. Three tiles from the stairs are missing, the fourth one is broken. Locus 1 – The Western Wall: Fig. 13 Close to the ceiling the gypsum lining, 1,5 cm thick, is missing. The plaster is dirty, traces of damp patches. In the upper part the plaster is doming off. At least six cracks of the plaster going from the top, including one in the middle of the locus 14 doorway. In a strip up 1,5 m high above the floor level the plaster has many air bubbles, and is coming off the wall. Locus 2 – Floor: Fig. 14 Beaten, cracked and unsmoothed mud; some rubbish. Locus 2 – Ceiling: Fig.15 Reed mats supported by wooden beams; both are moist. The mats are torn up in several places. Locus 2 – The Northern Wall: Fig. 16 The plaster is dirty; in the lower part thickening of the unsmoothed plaster. Locus 2 – The Eastern Wall: Fig. 17 The plaster is dirty and unsmoothed; thickened area and detachment in the lower part. The locus 3 doorway: the plaster is dirty, numerous scratches; in the lower part the plaster is peeling off and splitting off; a crack in the eastern part. Locus 2 – The Southern Wall: Fig. 18 The plaster is dirty; in the lower part thickening of the unsmoothed plaster. In the south-western corner large fragments of the plaster are falling off. Locus 2 – The Western Wall: Fig. 19 The plaster is dirty. In the lower part the plaster is badly damaged (detachment and peeling off). Locus 3 – Floor: Fig. 20 Beaten, unlevelled mud layer; some sand and rubbish on the top. Locus 3 – Ceiling: Fig. 21 The wooden beams are moist; some of them are cracked lengthwise; the southernmost one is bent down. Reed mats in some places are torn up. Locus 3 – The Northern Wall: Fig. 22 Close to the ceiling the gypsum lining is missing. In the western part some damp patches and some dirt. In the middle there is a crack 1,5 m long just above the locus 4 doorway, going down from the ceiling. Small cracks and air bubbles in the lower part of the wall. The locus 4 doorway: some dirt and traces of detachment. Locus 3 – The Eastern Wall: Fig. 23 Close to the ceiling the gypsum lining is missing. Some dirt and damp patches. Horizontal crack of the plaster at the height 1 m below the ceiling. A crack 5-6 cm wide in the north-eastern corner. A crack 5-15 cm wide in the upper part of the south-eastern corner. In a strip up to 0,8 m above the floor level there are air bubbles and detachment of the plaster. Locus 3 – The Southern Wall: Fig. 24 Close to the ceiling the gypsum lining is missing. Some dirt, damp patches and traces of rain water. Two vertical cracks of the plaster in the lower part. Peeling off of the plaster in the lower part. Locus 3 – The Western Wall: Fig. 25 Close to the ceiling the gypsum lining is missing. Some dirt, damp patches, traces of rain water. Two cracks of the plaster, including one over the locus 2 doorway. In the lower part - peeling off and detachment of the plaster. Locus 4 – Floor: Fig. 26 Made of a cement (?) bricks, in good state of preservation, covered with sand and rubbish layer. Two wires are standing out. Locus 4 – Ceiling: Fig. 27 Wooden beams and reed mats are moist. An electric wire is hanging down. Locus 4 – The Northern Wall: Fig. 28 Two vertical cracks, going from the ceiling. The plaster is damaged in a strip up to 1,5 m high above the floor level: is peeling off, partially has already fallen off. Locus 4 – The Eastern Wall: Fig. 29 The plaster is slightly soiled. There is a crack over the exit. In a strip up to 1 m high above the floor level the plaster has many air bubbles, is peeling off and cracking. In the exit doorway: some bricks and the gypsum lining of both walls are missing, probably the very place of fastening of the missing doors; the mud plaster with cement admixture (?); cracks on the southern wall; on both walls in the lower part the plaster is partially washed away, some bulges. Locus 4 – The Southern Wall: Fig. 30 One large and a few smaller vertical cracks, mainly going from the ceiling. The plaster is deteriorated in the lower part, especially in the south-western corner: is peeling off, there are air bubbles and detachment of the plaster. Locus 4 – The Western Wall: Fig. 31 Small spider’s webs in the lower part. Two vertical cracks of the plaster, including one over the locus 16 doorway. In a strip up to 1,4 m high above the floor level – there are some air bubbles, detachment of the plaster and tiny cracks. The locus 16 doorway: the mud plaster with straw temper and cement admixture (?); in the northern part at the floor there is detachment of the plaster in a form of air bubble; some losses of the plaster. Locus 5 – Floor: Fig. 32 Made of cement (?) bricks; in good state of preservation, packed up with wooden, mostly broken, chairs. Locus 5 – Ceiling: Fig. 33 Wooden beams and reed mats are wet. Several beams are cracked lengthwise. Locus 5 – The Northern Wall: Fig. 34 Five vertical cracks going from the ceiling throughout two third of the wall. The plaster is damaged in a strip up to 2,5 m high above the floor level: is peeling off, there are some air bubbles, and some fragments are missing. Locus 5 – The Eastern Wall: Fig. 35 Three vertical cracks going from the ceiling throughout two third of the wall. The plaster is damaged in a strip up to 2,5 m high above the floor level: is peeling off, there are some air bubbles and some fragments are missing. Locus 5 – The Southern Wall: Fig. 36 The plaster is damaged in a strip up to 2,5 m high above the floor level: is peeling off, there are some air bubbles and some fragments are missing. Locus 5 – The Western Wall: The plaster is damaged in a strip up to 1,3 m high above the floor level: is peeling off, there are some air bubbles and some fragments are missing. The locus 16 doorway: the mud plaster with straw temper and cement admixture (?); on both sides the plaster is damaged in a strip between 0,5 m and 2 m above the floor level, partially it has already fallen off; some fragments of the plaster are also missing in the southern part at the floor. Locus 6 – Floor: Fig. 37 Beaten mud, some sand and rubbish on the top. Locus 6 – Ceiling: Fig. 38 Wooden beams and reed mats are moist. Several beams are cracked lengthwise; on one beam a bird is sleeping. Locus 6 – The Northern Wall: Fig. 39 Three round air openings in the upper part of the wall. Several vertical cracks, going down from the ceiling. The plaster is damaged in a strip up to 2,2 m high above the floor: is coming off, has many cracks, is peeling off, and falling off . Locus 6 – The Eastern Wall: Fig. 40 The plaster is dirty, covered with spider’s webs. 2 m above the floor the plaster has come off from the wall throughout the width of the wall; below some air bubbles, detachment of the plaster and peeling off. Locus 6 – The Southern Wall: Fig. 41 A few vertical cracks, going down from the ceiling. 2 m above the floor level the plaster has come off from the wall throughout the width of the wall; below some air bubbles, detachment of the plaster and peeling off. Locus 6 – The Western Wall: Fig. 42 In a strip up to 2 m high above the floor level the plaster is peeling off and falling off. The locus 16 doorway: some fragments of the plaster are missing, especially in the northern part. Locus 7 – Floor: Fig. 43 The mud plaster with cement admixture (?), unsmoothed, a few cracks, some rubbish. Locus 7 – Ceiling: Fig. 44 Wooden beams and reed mats are moist. The mats are torn up in four places. A pipe running to the roof is located in the eastern part. Locus 7 – The Northern Wall: Fig. 45 The gypsum lining soiled, small losses. In a strip up to 1,3 m high above the floor – the plaster lost its white colour, is peeling off, splitting off and falling off. A crack 2-4 mm wide throughout the wall in the middle of the wall. Some electric installation: broken socket, two wires. Locus 7 – The Eastern Wall: Fig. 46 The plaster is dirty. 2,5 m above the floor level a horizontal bulge of the plaster; the plaster is splitting off, peeling off and falling off. At the floor – the plaster is cracked. Locus 7 – The Southern Wall: Fig. 47 The plaster is dirty; some traces of damp patches. Two crack of the plaster, including one at the height of two third of the wall, going down from the ceiling. In a strip up to 2,5 m high above the floor level – the plaster has a lot of air bubbles, is peeling off and falling off; there are thickened areas of the plaster and it is unsmoothed. Three round air openings, and a lamp-socket. At the floor an electrical wire. Locus 7 – The Western Wall: Fig. 48 The plaster is dirty, small damages in the lower part. Large crack of the plaster in the north-western corner. The locus 8 doorway: up to 2,2 m high above the floor level on the southern side – the plaster is deteriorated, there are some bulges, air bubbles and thickened areas. Locus 8 – Floor: Fig. 49 The mud plaster with cement admixture (?); some sand and rubbish. Locus 8 – Ceiling: Fig. 50 Wooden beams and reed mats are moist. Three beams are cracked lengthwise; the mats are torn up in three places. Locus 8 – The Northern Wall: Fig. 51 The plaster is dirty; some spider’s webs. The plaster is cracked in seven places, going from the ceiling nearly to the floor. In a strip up to 1 m high above the floor level the plaster is damaged: there are some cracks, it is peeling off and falling off. Locus 8 – The Eastern Wall: Fig. 52 The plaster is dirty; numerous spider’s webs. There is a crack throughout the wall above the locus 7 doorway. The plaster is deteriorated in a strip up to 2,2 m high above the floor level in the southern part – thickened areas, cracks and detachment. Locus 8 – The Southern Wall: Fig. 53 The plaster is dirty; traces of rain water. Vertical cracks of the plaster, including one above the locus 16 doorway. In a strip up to 2 m high above the floor level the plaster is deteriorated: there are air bubbles, the plaster is peeling off and splitting off. The locus 16 doorway: in a strip up to 1,5 m high above the floor level the mud plaster is damaged, unsmoothed, there are some buldges and detachment of the plaster. Locus 8 – The Western Wall: Fig. 54 The plaster is dirty, some spider’s webs. Two vertical cracks of the plaster. In a strip up to 2 m high above the floor level the plaster is deteriorated, horizontal detachment from the core of the wall throughout the wall, cracks and thickened areas. Locus 9 – Floor: Fig. 55 Some loose soil and rubbish. Locus 9 – Ceiling: Fig. 56 Wooden beams and reed mats are moist. Four beams are cracked lengthwise; reed mats are torn up in three places. Locus 9 – The Northern Wall: Fig. 57 The plaster is dirty; small spider’s webs. Two cracks, including one in the middle throughout the wall. In the lower part the plaster is peeling off, small damages. Inscriptions scratched in Arabic alphabet. Locus 9 – The Eastern Wall: Fig. 58 The plaster is dirty, small spider’s webs. In a strip up to 1,4 m high above the floor there are some air bubbles, cracks; the plaster is unsmoothed and is peeling off. Locus 9 – The Southern Wall: Fig. 59 The plaster is dirty, traces of damp patches. The plaster above the locus 16 doorway is cracked. In a strip up to 1,4 m high above the floor level, the plaster is seriously damaged, cracked, unsmoothed; it is peeling off and splitting off. The locus 16 doorway: in a strip up to 1,5 m high above the floor level, the mud plaster is cracking, splitting off and falling off. Locus 9 – The Western Wall: Fig. 60 The plaster is dirty, traces of damp patches and spider’s webs. In a strip up to 1,4 m high above the floor level the plaster is deteriorated; it is unsmoothed, cracked with air bubbles and is coming off. The locus 10 doorway: on the southern side the plaster is damaged, cracked, with air bubbles and is coming off. Locus 10A – Floor: Fig. 61 Loose sand with admixture of some gravel. Locus 10A – Ceiling: Fig. 62 Wooden beams and reed mats are very moist, large water drops (surface condensation?) are visible. Five or six beams are cracked lengthwise. Locus 10A – The Northern Wall: Fig. 63 The plaster is dirty; some spider’s webs. Except two major cracks, the state of the plaster is quite good. Locus 10A – The Southern Wall: Fig. 64 The plaster is dirty. One bigger crack of the plaster going down from the ceiling. A strip up to 1,2 m high above the floor level covered with mud plaster with cement (?) admixture: unsmoothed, cracked with some losses. A loss of the plaster measuring 20 x 15 x 10 cm. Locus 10B – Floor: Fig. 65 Covered with gravel and small stones; one larger stone, fragments of mud bricks, some rubbish. Locus 10B – Ceiling: Fig. 66 Wooden beams and reed mats are very moist; large water drops are visible (surface condensation?). Lack of mats above three beams from the South – rain water is coming easily inside. Locus 10B – The Northern Wall: Fig. 67 The plaster is dirty; some spider’s webs. Generally good state of preservation. Locus 10B – The Eastern Wall: Fig. 68 The plaster is dirty; small spider’s webs, single damp patches. Six large crack of the plaster. A strip up to 1,5 m high above the floor level covered with the plaster with cement (?) admixture. At the floor the plaster is cracked, is peeling off and falling off. Locus 10B – The Southern Wall: Fig. 69 Covered with mud washed away from the roof (?) and carried over by rain water. Five large horizontal cracks. In a strip up to 1,8 m high above the floor level – the plaster is coming off, peeling off and falling off. Locus 10B – The Western Wall: Fig. 70 The plaster is dirty; tiny spider’s webs. Strong horizontal and vertical cracks. In the middle part there are air bubbles, detachment from the core of the wall, cracks, some fragments have already fallen off. In a strip up to 0,7 m high above the floor level there is the plaster with cement (?) admixture; unsmoothed and unlevelled. Some the plaster losses at the floor. Locus 10C – Floor: Fig. 71 Loose sand; some rubbish. Locus 10C – Ceiling: Fig. 72 Wooden beams and reed mats are moist. The reed mats are torn up in two places. Locus 10C – The Northern Wall: Fig. 73 Stairs to the roof (23 steps) covered with the plaster with cement admixture; partially obliterated some ruble on the surface. Locus 10C – The Eastern Wall: Fig. 74 The plaster is dirty; tiny spider’s webs. A few cracks; the plaster is peeling off at the floor. Locus 10C – The Western Wall: Fig. 75 The plaster is dirty; traces of damp patches. Bulges, serious cracks, losses of the plaster in the middle part. A considerable plaster loss at the step of the stairs. Locus 11 – Floor: Fig. 76 Loose soil with admixture of gravel. Locus 11 – Ceiling: Fig. 77 Wooden beams and reed mats are very moist; large water drops are visible (surface condensation?). Locus 11 – The Northern Wall: Fig. 78 The plaster is dirty; tiny spider’s webs. One vertical crack. The plaster is deteriorated, is peeling off and falling off in the north-eastern corner up to 1,2 m high above the floor level. Locus 11 – the Eastern Wall: Fig. 79 The plaster is dirty; one crack. In a strip up to 1 m above the floor level and to the North of the locus 12 doorway the plaster has air bubbles, is detached and is peeling off; one small but deep (10 m) hole in the plaster. In a strip up to 1 m high above the floor level and to the South of the locus 12 doorway there is a plaster with cement (?) admixture, unsmoothed; it supplements the loss of the gypsum lining. At the floor the plaster is cracked and is peeling off. The locus 12 doorway: three cracks, in the lower part some supplements made out of cement (?) plaster. Locus 11 – the Southern Wall: Fig. 80 The plaster is dirty; tiny spider’s webs. Several horizontal and vertical cracks. Nests of insects (?) made of fragile mud. Deterioration of the plaster at the floor. Locus 11 – The Western Wall: Fig. 81 The plaster is dirty; small spider’s webs. A large vertical crack in the middle throughout the wall; it is accompanied by a bulge and peeling off the plaster. Several additional vertical cracks. The plaster is missing in three places. In the southern part at the floor the plaster with cement admixture is applied on a surface measuring 1 by 1,5 m Locus 12 – Floor: Fig. 82 Loose sand. Locus 12 – Ceiling: Fig. 83 Wooden beams and reed mats are very moist; large water drops are visible (surface condensation?). A few beams cracked lengthwise. Locus 12 – The Northern Wall: Fig. 84 There is some dirt on the plaster and small spider’s webs. A strip up to 1,8 high above the floor level is covered probably with the second layer of the gypsum lining; it is unlevelled and unsmoothed. The plaster is peeling off at the floor. Locus 12 – The Eastern Wall: Fig. 85 There is some dirt on the plaster and tiny spider’s webs. A strip up to 1,8 m high above the floor level and to the North of the locus 13 doorway is covered with the second layer of unsmoothed plaster. Two small cracks; in one place the plaster is peeling off. To the South of the locus 13 doorway there is a second layer of unsmoothed plaster. The locus 13 doorway: some dirt, traces of the second layer of the plaster. Scratches on the plaster. Locus 12 – The Southern Wall: Fig. 86 The plaster is dirty, small spider’s webs. One horizontal crack of the plaster. Locus 12 – The Western Wall: Fig. 87 The plaster is dirty; tiny spider’s webs. One serious, vertical crack of the plaster. A new unlevelled and unsmoothed layer of plaster is applied in the lower part. Locus 13 – Floor: Fig. 88 Sand, grit, fragments of the plaster fallen down, some rubbish. Locus 13 – Ceiling: Fig. 89 Wooden beams and reed mats are very moist; large water drops are visible (surface condensation?). Several beams are cracked lengthwise. Locus 13 – The Northern Wall: Fig. 90 The plaster is dirty, several damp patches. A strip up to 1,2 m high above the floor level is badly damaged: the plaster is peeling off, coming off and cracking. Two large plaster losses (0,7 m in diameter each). Locus 13 – The Eastern Wall: Fig. 91 The plaster is dirty, several damp patches. A loss of the plaster (0,4 m in diameter) close to the ceiling. The plaster is peeling off at the floor. The locus 14 doorway: small losses of the plaster, especially from the southern part close to the floor; insect nets made out of mud; in the northern part the plaster is unsmoothed. Locus 13 – The Southern Wall: Fig. 92 The plaster is dirty, some damp patches and spider’s webs. One vertical crack. Small scratches and losses of the plaster, especially at the floor. Locus 13 – The Western Wall: Fig. 93 The plaster is dirty, some damp patches and spider’s webs. The plaster is missing in a strip measuring 0,3 by 2,2 m close to the ceiling. The plaster in a strip up to 1,2 m high above the floor level is damaged: cracks, the plaster is peeling off and falling off. Several vertical cracks. A loss of the plaster (1 m in diameter) to the North of the locus 12 doorway. Locus 14 – Floor: Fig. 94 Loose sand, some rubbish. Locus 14 – Ceiling: Fig. 95 Wooden beams and reed mats are moist. The mats are torn up in two places. Locus 14 – The Northern Wall: Fig. 96 The plaster is slightly dirty; small spider’s webs. One vertical crack in the eastern part. Small cracks and losses of the plaster in the lower part. The locus 15 doorway: the plaster is peeling off, cracking and falling off especially in the western part. Locus 14 – The Eastern Wall: Fig. 97 The plaster is a little bit dirty; tiny spider’s web. Small losses and cracks in the lower part. The locus 1 doorway: air bubbles, cracks and losses of the plaster, especially from the North. Inscriptions scratches in the Latin alphabet. Locus 14 – The Southern Wall: Fig. 98 The plaster is a little bit dirty. In the middle of the wall a crack going for two third of the wall height. In a strip up to 1,1 m high above the floor level the plaster is unsmoothed, is peeling off and falling off. Locus 14 – The Western Wall: Fig. 99 The plaster is a little bit dirty. Two vertical cracks above the locus 13 doorway. The plaster is unsmoothed in the lower part. Locus 15 – Floor: Fig. 100 Beaten soil, unlevelled with fragments of plaster, some rubbish. Locus 15 – Ceiling: Fig. 101 Wooden beams and reed mats are moist. Locus 15 – the Northern Wall: Fig. 102 The plaster is a little bit dirty. The plaster is cracked, unsmoothed and has air bubbles in the lower part. A strip of the plaster up to 0,4 m high above the floor level has fallen off. The locus 16 doorway: covered with cement (?) plaster; in the lower part the plaster has split off and cracked; some places of the plaster losses. Locus 15 – the Eastern Wall: Fig. 103 The plaster is dirty. In a strip up to 2 m high above the floor level – the plaster has air bubbles, is detached from the core of the wall and has vertical cracks. Locus 15 – The Southern Wall: Fig. 104 The plaster is a little bit dirty; some spider’s webs. In a strip up to 1,2 m high above the floor level – the plaster is unsmoothed and cracked; there are some losses and detachment of the plaster. Locus 15 – The Western Wall: Fig. 105 The plaster is a little bit dirty. A vertical, clearly visible crack of the plaster. The plaster is peeling off and powdering in the lower part. At the height of 1,8 m high above the floor level the plaster is unsmoothed, has some air bubbles and cracks. Locus 16 – Floor: Fig. 106 Covered with baked bricks (?); good state of preservation. There is a well in the north-eastern corner; its outside cover is made out of a cement mortar; in the inside – there are losses of the brick fragments; the surface is wet and there is some rubbish. A large water pool near the well occupies one third of the surface. Locus 16 – The Northern Wall: Fig. 107 The plaster is missing in five places close to the roof. In a strip up to 2 m high above the floor level the plaster is cracked in some places, and there are medium-sized losses, especially at the bottom. Substantive losses of the plaster in the eastern part of the locus 9 doorway and in a part of the locus 8 doorway. Inscriptions in Latin alphabet scratched on the plaster. Locus 16 – the Eastern Wall: Fig. 108 Large losses of the mud plaster in three places close to the roof; baked bricks are visible in the wall. The outsider layer of the plaster is washed away. A crack on the plaster between the locus 5 doorway and the locus 6 doorway. A considerable part of the plaster is missing between entrances to the loci 4 and 5. Moisture content and some losses of the plaster at the floor. Locus 16 – the Southern Wall: Fig. 109 The plaster is in a bad state of preservation; numerous cracks, the plaster is peeling, especially between the entrances to the loci 1 and 15. A strip of the plaster measuring 2 m by 0,7 m is missing above the locus 15 entrance, close to the floor. Losses of the plaster in the eastern part. A strip up to 1,2 m high above the floor level is moist; the plaster is washing away at the floor. Moisture content is also visible between the entrances to the loci 1 and 15 in the upper part. Inscriptions in Latin alphabet scratched. Locus 16 – The Western Wall: Fig. 110 Bad state of preservation the plaster fragments close to the roof – serious losses also in the lower part. Cracks and detachment of the plaster above the entrances to the loci 17 and 21. The plaster around the locus 17 entrance is peeling off, splitting off and falling off. A strip up to 0,7 m high above the floor level is moist; there are some losses of the plaster, especially at the base of the wall; the plaster is washing away by rain water. Locus 17 – Floor: Fig. 111 Made out of cement tiles or baken bricks; packed up with broken wooden chairs; some rubbish. Locus 17 – Ceiling: Fig. 112 Wooden beams and reed mats are moist. Three cracked beams, almost on the whole length. The mats are torn up in three places. Locus 17 – The Northern Wall: Fig. 113 The plaster is a little bit dirty; small spider’s webs. Three vertical cracks above the locus 21 entrance. In a strip up to 1,4 m high above the floor level the plaster has a bulge; it is cracked and unsmoothed. The locus 21 doorway: two cracks of the plaster; there are air bubbles in a strip up to 1,2 m above the floor level; the plaster is peeling off and falling off. Locus 17 – the Eastern Wall: Fig. 114 Tiny spider’s webs. There are cracks and air bubbles close to the ceiling and in the lower part to the North of the locus 16 doorway; the plaster is peeling off and falling off. The locus 16 doorway: some looses of the mud plaster in the lower part; there are buldges and cracks. Locus 17 – The Southern Wall: Fig. 115 Minute spider’s webs. A crack in the middle of the wall, above the locus 20 doorway. Some cracks and losses of the plaster in the lower part. The locus 20 doorway: in a strip up to 1,2 m high above the floor level the plaster is detached, cracked and some fragments are missing. Locus 17 – The Western Wall: Fig. 116 Tiny spider’s webs. Two cracks of the plaster. In a strip up to 1,5 m high above the floor level the plaster is deteriorated; there are air bubbles, cracks and the plaster is peeling off and falling off. Locus 18 and locus 19 – inaccessible because packed up with wooden chairs. Fig. 117 Locus 20 – Floor: Fig. 118 Loose and moist soil. Locus 20 – Ceiling: Fig. 119 Wooden beams and reed mats are wet; the mats are torn up in one place. Locus 20 – The Northern Wall: Fig. 120 The plaster is dirty. In four places in the lower part the plaster is coming off, cracking and falling off. Locus 20 – The Eastern Wall: Fig. 121 The plaster is a little bit dirty. A crack above the locus 16 entrance. In the lower part the plaster is unlevelled and unsmoothed. The locus 16 doorway: the mud plaster damaged in the lower part (air bubbles, cracks), especially in the northern part where some losses of 10-15 cm deep. Locus 20 – The Southern Wall: Fig. 122 The plaster is a little bit dirty. In a strip up to 1,5 m high above the floor level the plaster is unsmoothed, and there are some cracks and air bubbles. Locus 20 – The Western Wall: Fig. 123 The plaster is a little bit dirty. Three vertical cracks at the two third of the wall height, going down from the ceiling. In a strip up to 1,5 m high above the floor level the plaster is unsmoothed, has some cracks and air bubbles. Locus 21 – Floor: Fig. 124 Loose soil, three hollows; packed up with wooden chairs. Locus 21 – Ceiling: Fig. 125 Wooden beams and reed mats are moist. Locus 21 – the Northern Wall: Fig. 126 The plaster is dirty. In a strip up to 2 m high above the floor level the plaster is damaged: it has some air bubbles and losses and is coming off and peeling off. Locus 21 – The Eastern Wall: Fig. 127 The plaster is a little bit dirty. Two cracks above the locus 16 doorway. In a strip up to 2 m high above the floor level the plaster is damaged: there are some losses, air bubbles, it is coming off and peeling off. The locus 16 doorway: plaster bulge in the southern part, the plaster is damaged in a strip up to 1,6 m high above the floor level on the southern wall. Locus 21 – The Southern Wall: Fig. 128 The plaster is dirty. A crack above the locus 17 doorway. In a strip up to 2 m high above the floor level the plaster is damaged: there are some losses, air bubbles, it is coming off and peeling off. Locus 21 – The Western Wall: Fig. 129 The plaster is a little bit dirty. Two vertical losses above the locus 22 doorway. In a strip up to 2 m high above the floor level the plaster is damaged: there are some losses, air bubbles, it is coming off and peeling off. The locus 22 doorway: the plaster is damaged, is coming off and peeling off. Locus 22 – inaccessible because it is packed up with wooden chairs. Fig. 130 Description elaborated on 4th–6th November 2004, photographs taken on 16th-17th November 2004 and translated into English on 24th-27th November 2004 by Mirosław OLBRYŚ (Poland). The photograph no. 5 was taken by Agnieszka Dolatowska in July 2004. Edited by George Gogolewsky.

# Text boxes

A

B

C

16